RTL-SDR manual gain control

RTL-SDR rf_gain table (29 values)
0.0	0.9	1.4	2.7	3.7	7.7	8.7	12.5	14.4	15.7	16.6	19.7	20.7	22.9	25.4	28.0	29.7	32.8	33.8	36.4	37.2	38.6	40.2	42.1	43.4	43.9	44.5	48.0	49.6
	0.9	0.5	1.3	1.0	4.0	1.0	3.8	1.9	1.3	0.9	3.1	1.0	2.2	2.5	2.6	1.7	3.1	1.0	2.6	0.8	1.4	1.6	1.9	1.3	0.5	0.6	3.5	1.6

Input rf signal is voltage level, need to convert to power level to determine its dB. Based on parameters in librtlsdr, the gain values are not linear, but depend on values. So in order to adjust the gain control, the different gain values need to take into acount.

Steps:
1. keep track of the current manual gain index, and its upper & lower cap.
Example: at gain_idx = 0, there is no room to reduce gain further, and thus if the signal exceed the upper limit, nothing can be done, except to put a remark on signal clipping…
And when signal goes lower than lower_cap, it can change to the next gain idx. The lower_cap and upper_cap value are dynamically determined, depending on its current gain_idx.

gain_idx	gain_val	gain_diff	Voltage	Vdiff = 10^(db/20)
0	0		1.00		Let assume the signal voltage level at gain_idx_0 = 1. Then the signal voltage needs an increase of 1.11 to get the equivalent 0.9dB power increase
1	0.9	0.9	1.11	1.11
2	1.4	0.5	1.17	1.06
3	2.7	1.3	1.36	1.16
4	3.7	1	1.53	1.12
5	7.7	4	2.43	1.58
6	8.7	1	2.72	1.12
7	12.5	3.8	4.22	1.55
8	14.4	1.9	5.25	1.24
9	15.7	1.3	6.10	1.16
10	16.6	0.9	6.76	1.11
11	19.7	3.1	9.66	1.43
12	20.7	1	10.84	1.12
13	22.9	2.2	13.96	1.29
14	25.4	2.5	18.62	1.33
15	28	2.6	25.12	1.35
16	29.7	1.7	30.55	1.22
17	32.8	3.1	43.65	1.43
18	33.8	1	48.98	1.12
19	36.4	2.6	66.07	1.35
20	37.2	0.8	72.44	1.10
21	38.6	1.4	85.11	1.17
22	40.2	1.6	102.33	1.20
23	42.1	1.9	127.35	1.24
24	43.4	1.3	147.91	1.16
25	43.9	0.5	156.68	1.06
26	44.5	0.6	167.88	1.07
27	48	3.5	251.19	1.50
28	49.6	1.6	302.00	1.20

Let consider 3 scenarios:

gain_idx = 0
- if the rf signal is too large and being clipped, nothing can be done other than reporting.
- if rf signal is small, can increase gain by change to next gain_idx. How to determine whether signal is small ? Let’s take a criteria that if signal is less than 3dB of max level (equivalent to voltage is 1.42 time less = 127.5/1.4142 +127.5, then increase the gain. The signal level after gain increased still have to fall within limit, i.e. less than max_level of let say 15%

graph illustrating positive half of signal amplitude:
|--- upper limit (127)
|----------- 85%
|
|
|
|--- lower limit
|
|
|--- 0 (or more accurately -0.5)

for a given signal level, just check the level and perform:
- if within ok range: do nothing
- if below ok range: evaluate to decide whether to increase gain
- if above ok range: evaluate to decide whether to reduce gain

So what is ok range: let take 3dB gain. The signal would be from 0.707 to 0.9. If the signal goes below 0.707
MAX_CAP = 127
UPPER_CAP = 115
LOWER_CAP = 90

If signalMax < LOWER_CAP,
- check if next gain_increase would cause exceeding MAX_CAP, if not exceeding, go to next gain, if exceeding, do nothing.

If signalMax > UPPER_CAP,
- check if next gain_descrease would cause signal below LOWER_CAP, if not then go to next gain_descrease, otherwise stay there – do nothing

If signalMax = MAX_CAP, go to next gain_decrease.

How to determine signalMax: the highest value (or lowest value 0-255), with at least 1 occurance. Or to avoid error, can be adjust to N=3 or 5, ... occurrence.